## Slide 1: Way forward on coexistence tests for LAA
Ericsson, Qualcomm
3GPP TSG-RAN WG4 Meeting #77 R4-158280 Anaheim, CA, USA, 16–20 November, 2015

## Slide 2: Content
This way forward contains the following:
  General principles
  LBT parameters and Requirements
  LBT tests
  Multi-node tests
  Time plan

## Slide 3: Way forward on general principles
All tests should be conductive tests for LAA.
One example of such test setup is given below.

## Slide 4: Specifying LBT parameters
Specify the following requirements in 36.104
  LBT BW: The LBT bandwidth will be 20MHz, as it is agreed so far.
  Energy detection thresholds: depends on RAN1
  Maximum channel occupancy time: depends on RAN1
  LBT measurement accuracy requirement (the feasibility of the following test should be studied): The Base Station should be able to assess whether the medium is busy or idle within X microseconds and with at least Y% probability.
Note: Parameters which depend on RAN1 decisions can be revisited later.

## Slide 5: LBT tests
Capability to perform Energy detection, includes following tests:
  performance of energy detection thresholds, and
  maximum channel occupancy time.
The above tests will cover the parameters in previous slide
LBT tests will ensure that LAA coexistence targets are met and hence fair coexistence with Wi-Fi

## Slide 6: Multi-node tests
RAN4 will study the need and complexity of introducing multi-node tests, which represent additional test compared to the essential LBT related tests
If needed, multi-node test can be initiated in performance part of the WI and may test coexistence with
  other wireless systems using the spectrum, e.g. Wi-Fi, and
  other LAA operators operating in the spectrum

## Slide 7: Time plan
Following time plan can be followed:
Tests | Core part of WI (until December 2015) | Performance part of WI (until June 2016)
LBT tests | Minimum requirements are documented in 36.104 | Details of actual test procedures to be defined and documented in 36.141
Multi-node tests |  | Study of type of test and test procedure. Details of possible test procedures to be defined and documented